A V8 conversion for an M Series TVR

Some years after selling my old TVR Vixen I had the opportunity to buy a 1600M but I was disappointed when I started to draw comparisons with the old Vixen.

| 1970 TVR Vixen | 1974 TVR 1600M |
| --- | --- |

There were many aspects that I liked but the performance was disappointing, so I decided to go for an engine transplant. 
    The choices were between a tuned original Ford Kent engine, converting the car to a 3000M by installing one of the Ford V6s, or a V8.  I chose the aluminium Rover/Buick engine. 
The following table compares some of the figures that led to that solution.

|  | bhp | Maximum Torque (lb. ft..) | Useful rev range (rpm) | bmep (psi) |
| --- | --- | --- | --- | --- |
| Original Ford Kent 1600cc | 86 at 5500rprn | 92 at 4OOOrpm | 1500 rpm | 142 |
| Tuned Ford Kent 1700cc | 156 at 7000rpm | 130 at 57O0rpm | 1300 rpm | 190 |
| TVR 3000M Ford Essex V6 | 138 at 5000rpm | 174 at 3000rpm | 2000 rpm | 144 |
| Ford Capri Cologne V6 | 160 at 5700rom | 162 at 4300rpm | 1400 rpm | 134 |
| American Ford V8 4700cc | 175 at 4400rpm | 254 at 2400rpm | 2000 rpm | 134 |
| Ford V8 4700cc High Comp | 243 at 6500rpm | 283 at 3400rpm | 3100 rpm | 149 |
| Rover V8 3500cc | 155 at 5250rpm | 198 at 2500rpm | 2750 rpm | 140 |

Notes:

- The “tuned Kent” figures are for a very high tuned unit - probably unsuitable for road use.

- The American Ford V8 figures are 90% of the normally quoted “gross” figures to compare with the DIN figures used for the European engines.

For the non technical the following explanation of the figures may be useful.

- bhp - This is the maximum power that the engine can develop.   It gives a comparative indication of the cars ultimate top speed.

- Max. Torque - Torque and power are related by the formula rpm x torque = 5252 x power where power is in hp and torque is in lb.ft.   Maximum torque is the maximum capacity to accelerate the car.

- bmep - Brake mean effective pressure is a calculated value of the effective pressure in the cylinder.   The higher the value, the more efficient is the engine.

- Useful rev range - This is simply the difference between the maximum torque revs and the maximum bhp revs.  The larger the band the less gear changing will be required for a road car.

Having decided on the power unit, the obvious choice for gearbox was the Rover 5 speed unit used in the manual  SD1.  A single advertisement in the the local paper resulted in a rusty 1977 SDI with manual gearbox.  The car was duly gutted, everything useful stored and the shell despatched to the local scrap dealer. 
    One weekend later the bonnet was off the 1600M.  The Kent engine, gearbox and prop shaft out, and the big V8 was being lowered into the TVR engine bay. 
    At that stage I started to get anxious.   As the engine was lowered, the first item to touch was the alternator - so I took it off.   Then the oil pump fouled - again, took it off.  When the engine, or what was left of it, was eventually in the engine bay the garage floor was littered with water pumps, front pulley, oil pump, gear change mechanism and alternator. 
    After a few weeks of head scratching, sketching, and metal bashing, most of the problems were solved.   The alternator on the SD1 engine is mounted in front of the engine, and low down. right where the TVR frame sits.  To overcome this, I adapted the brackets from the old Rover 3500 engine to accept the longer 17ACR Lucas alternator from the SD1.  This placed the alternator above the level of the chassis. 
   The problem of the oil pump fouling the lower chassis cross member was solved by fitting an MGB GT V8 l pump and remote filter. 
    Engine mounts were fabricated and the Rover rubbers used upside-down. 
    The only real head-scratcher was the gearbox.  The gearchange aligned perfectly with rear parcel shelf!   To solve that problem I had to cut down the extension casting and make my own short gearshift extension. 
    The next area to look at was the exhaust manifolds.   Armed with lots of photographs and a full size drawing of the space available (or more accurately the lack of space available), I went to see Maniflow in Salisbury who make a manifold for the V8 Tasmin.   I came away satisfied that they could do the job it I could get the car to them. 
    I had now convinced myself that it was feasible to get the big V8 into the space previously occupied by the 1600 engine.  The next stage was to remove the body from the chassis and finalize gearbox mounts, transmission, differential, and all the ancillaries. It is surprisingly easy to remove the body - ten nuts and bolts, disconnect the front wiring and steering and lift - easy! 
    As soon as I had welded on a couple of plates to attach the Rover gearbox mounting bracket, I was ready to take the rolling chassis  with engine and gearbox to Maniflow for the exhaust manifolds and pipes.

| Undo 10 bolts and lift! | Off to have the manifolds made |
| --- | --- |

Whilst this was going on I started thinking about the transmission and differential.  The 1600M was fitted with the factory option 4.75:1 differential in a TR6 case.   I t was easy to changed the ratio to 3.45:1 by fitting the differential from a Triumph 2500.   With this ratio the peak engine torque corresponds with the most useful speeds for gear changing as can be seen in the table below.

| Engine rpm. |  | Speed in | gears |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 1st | 2nd | 3rd | 4th | 5th |
| 1500 | 9 mph | 15 mph | 22 mph | 31mph | 38 mph |
| 2500 | 16 mph | 25 mph | 37 mph | 52mph | 63 mph |
| 3500 | 22 mph | 35 mph | 52 mph | 73 mph | 88 mph |
| 4500 |  | 45 mph | 67 mph | 94 mph | 114 mph |
| 5500 |  |  | 82 mph | 115 mph | 138 mph |

A new short propshaft was made by cutting down, re-welding and dynamically balancing a propshaft from an old Rover 3500 saloon.

| The Bare Chassis | The 3500 V8 with manifolds |
| --- | --- |

Once  I  had collected the chassis with the new manifolds, I was able to fit the transmission parts, rustproof and paint everything, overhaul the suspension and brakes and refit the chassis to the body.

The engine was overhauled and everything put back together.

How did it turn out?  Well the only way I can describe it is breathtaking.  Acceleration was in the supercar league, yet I could cruise effortlessly around in 4th or 5th gear listening to that lovely V8 burble from the wide bore twin exhausts.  Fuel economy was no worse than the 1600cc engine with 30mpg easily achievable on a run and an overall average over the first 3500 miles of exactly 25mpg.

| The finished V8 TVR | With its stablemate |
| --- | --- |

Would I recommend the conversion?  Well the fact that TVR eventually switched to the same engine for the less attractive Tasmin models that followed the M Series and are still using a derivative in the current models says it all.